## Slide 1: Q-1 Which one is more cheaper and Easy to Design and manufacture?
1- SIP (System in a Package)
2- POP (Package on a Package)
3- SOC (System on Chip)
4- SOM (System on module)

## Slide 2: Q-2 Which one is more Compact in size?
1- SIP (System in a Package)
2- POP (Package on a Package)
3- SOC (System on Chip)
4- SOM (System on module)

## Slide 3: Q-3 What is Bandwidth of Processor Data-transfer?
1- Maximum Data-Rate
2- Difference b/w Min & Max Data-Rate
3- Mean of Min & Max Data-Rate

## Slide 4: Q-4 Where we store Cache Data?
1- On DRAM
2- On SRAM
3- On External Cache Memory

## Slide 5: Q-5 What is Pre-Fetch Multiplier of DDR4 and LPDDR4?
1- 8n, 8n
2- 16n, 16n
3- 8n, 16n

## Slide 6: Q-6 #DQS (Data Strobe) Comes under which signal Group?
1- Data Group
2- Control Group
3- Command and Address Group
4- Clock Group

## Slide 7: Q-7 For 64 Bit total Data Width, what will be the rank of memory if each memory channel has 16 bit width?
1- 16
2- 4
3- 2
4- 8

## Slide 8: Q-8 if Clock freq. is 400Mhz, what will be the data rate for DDR3 (8n)?
1- 400x8x64/8 MT/S
2- 400X64/8 MT/S
3- 400X8X32/8 MT/S

## Slide 9: Q-9 What is the Min/Max Voltage supply for LPDDR4 for Logic 1?
1- 0.6V/1.1V
2- 0.1V/1.6V
3- 0.8/1.1V
4- 0.1/1.8V